## Slide 1: ESspice
SPICE implementation in C++ by Ethan Sifferman

## Slide 2: Specifications
3 Primary Classes:
MATLAB Interface
Circuit Netlist
Analysis (DC and TRAN)
Misc
Over 1200 lines of C++
Eigen Sparse Matrix Library Used https://eigen.tuxfamily.org/
Scalable and very fast!!!

## Slide 3: Example
// create matlab instance
matlab m;
// load circuit
string js = m.ckt_to_json(filename);
circuit a{js};
cout << "Finished loading circuit." << endl;
// Run circuit
auto run = a.run(&m);
tran tran_run(&a, .1, 3);
tran_run.plotnv(&m, 1);
tran_run.plotnv(&m, 2);

## Slide 4: MATLAB Engine
class matlab {
public:
class CouldNotStartMatlabEngine { };
matlab(); // start matlab engine
~matlab(); // close matlab engine
std::string ckt_to_json(const std::string & filename);
void show_plot(const std::vector<double> & data, const std::string & title, const std::string & xlabel, const std::string & ylabel, const double & xtick, const double & xlim);
private:
Engine * ep;
};

## Slide 5: Linear Element Hierarchy
struct linelem { enum ElemType_t { R = 'R', C = 'C', L = 'L', V = 'V', I = 'I' }; ElemType_t ElemType; std::string name; node *Node1, *Node2; }; struct resistor : linelem { double resistance; }; struct storage_device : linelem { }; struct capacitor : storage_device { double capacitance, initial_voltage; }; | struct inductor : storage_device { double inductance, initial_current; }; struct power_source : linelem { enum TYPE_t { DC = 0, PWL = 2 }; TYPE_t SOURCE_TYPE; }; struct V_source : power_source { }; struct V_dc : V_source { double voltage_value; }; | struct V_pwl : V_source { typedef std::vector< std::pair<double, double> > voltages_t; voltages_t voltages; }; struct I_source : power_source { }; struct I_dc : I_source { double current_value; }; struct I_pwl : I_source { typedef std::vector< std::pair<double, double> > currents_t; currents_t currents; };

## Slide 6: Analysis Base Class
class analysis {
public:
analysis(const circuit * const c);
enum TYPE_t {
DC = 0,
TRAN_FE = 1,
TRAN_BE = 2,
TRAN_TR = 3
};
virtual void plotnv(matlab * const m, const int & node_name) const = 0;
virtual void printnv(const int & node_name) const = 0;
protected:
// how accurate the simulation should be
static constexpr double precision = 0.000000001;
// Resistor added to every node
static constexpr double R__n = (0.5/precision);
const circuit * const c;
std::vector<circuit::linelem*> itrelems;
};

## Slide 7: DC Class
class dc : public analysis {
dc(const circuit * const c);
void plotnv(matlab * const m, const int & node_name) const;
void printnv(const int & node_name) const;
double voltage(const circuit::node * const n) const;
double voltage(const circuit::linelem * const e) const;
double current(const circuit::linelem * const e) const;
std::unordered_map< const circuit::linelem*, size_t > V_source_i;
std::unordered_map< const circuit::node*, double > node_voltage;
std::unordered_map< const circuit::capacitor*, double > capacitor_current;
std::unordered_map< const circuit::V_source*, double > V_source_current;
struct mosfet_solver {
static double conductance(const circuit::mosfet * const m, const double & V_GS, const double & V_DS);
static double I_DS(const circuit::mosfet * const m, const double & V_GS, const double & V_DS);
static double NR_G_eq(const circuit::mosfet * const m, const double & V_GS,const double & V_DS);
static double NR_I_eq(const circuit::mosfet * const m, const double & V_GS,const double & V_DS);
};
void stamp_A(Eigen::SparseMatrix<double> & A, const circuit::linelem * const e) const;
void stamp_z(Eigen::SparseMatrix<double> & z, const circuit::linelem * const e) const;
void stamp_A_NR(Eigen::SparseMatrix<double> & A_NR, const circuit::mosfet * const m, const double & V_GS, const double & V_DS) const;
void stamp_z_NR(Eigen::SparseMatrix<double> & z_NR, const circuit::mosfet * const m, const double & V_GS, const double & V_DS) const;
};

## Slide 8: TRAN Class
class tran : public analysis {
tran(const circuit * const c, const double & time_step, const double & stop_time);
void plotnv(matlab * const m, const int & node_name) const;
void printnv(const int & node_name) const;
double voltage(const circuit::node * const n, const int & t = -1) const;
double current(const circuit::linelem * const e, const int & t = -1) const;
static constexpr double tran_precision = 0.000000001;
std::unordered_map< const circuit::V_source*, size_t > V_source_i;
std::unordered_map< const circuit::node*, std::vector<double> > node_voltage;
std::unordered_map< const circuit::storage_device*, std::vector<double> > storage_device_current;
std::unordered_map< const circuit::V_source*, std::vector<double> > V_source_current;
struct storage_device_solver {
static double conductance(const circuit::capacitor * const c, const double & time_step);
static double conductance(const circuit::inductor * const l, const double & time_step);
};
struct mosfet_solver {
static double conductance(const circuit::mosfet * const m, const double & V_GS, const double & V_DS);
static double I_DS(const circuit::mosfet * const m, const double & V_GS, const double & V_DS);
static double NR_G_eq(const circuit::mosfet * const m, const double & V_GS, const double & V_DS);
static double NR_I_eq(const circuit::mosfet * const m, const double & V_GS, const double & V_DS);
};
void stamp_A(Eigen::SparseMatrix<double> & A, const circuit::linelem * const e) const;
void stamp_z(Eigen::SparseMatrix<double> & z, const circuit::linelem * const e) const;
void stamp_A_NR(Eigen::SparseMatrix<double> & A_NR, const circuit::mosfet * const m, const double & V_GS, const double & V_DS) const;
void stamp_z_NR(Eigen::SparseMatrix<double> & z_NR, const circuit::mosfet * const m, const double & V_GS, const double & V_DS) const;
double time_step;
double stop_time;
};

## Slide 9: Demonstration

## Slide 10: Questions?